CARUS( 3350 water treatment chemical is an effective corrosion inhibitor and sequestrant developed specifically for use in potable and industrial water systems.  This dry product is manufactured with the highest quality raw materials for sequestration and corrosion control.

- Controls iron and manganese, minimizing rusty or dirty water in the distribution system.

- Reduces discoloration, staining, and sediment buildup in the water system, resulting in fewer customer complaints.

- Diminishes calcium scale deposits typically seen in hot water lines and heaters.

- Lowers chlorine consumption, which controls biofilm regrowth and improves disinfection in the distribution system.

- Inhibits corrosion of steel distribution system water lines, iron and galvanized piping, and lead and copper plumbing.

- Decreases iron tuberculation, which can extend the life of the distribution system.

- Minimizes the occurrence of microbial-induced corrosion, providing longer system life.

- Saves money by reducing corrosion, lowering chlorine demand, and decreasing hydrant flushing, leaks, and failures.

- White granular solid

- Solubility (lbs./gal.): 2

- Bulk Density: 90 lbs./ft3

- Conforms to ANSI/NSF Standard 60

- NSF Maximum Feed Rate: 5 mg/L

CARUS( 3350 water treatment chemical is packaged and shipped in 50-pound (net weight) bags and pails.  Product containers should be kept tightly closed and stored in a dry, cool place when not in use.  The product should also be protected from excessive moisture.  Avoid contact with eyes, skin, and clothing.  For complete information, please refer to the Material Safety Data Sheet (MSDS).

CARUS( 3350 water treatment chemical is dissolved in a day tank and applied using a chemical metering pump.  Normal feed solutions are 1 pound per gallon.  For dosage rates or answers to technical questions, please call Carus Phosphates, Inc. at  (800) 929-6789.

# Text boxes

PROPERTIES AND CERTIFICATIONS

(CARUS and Design) is a registered service mark of Carus Corporation.

# CARUS™ is a trademark of Carus Corporation.

Responsible Care( is a registered service mark of the American Chemistry Council.

BENEFITS OF CARUS™ 3350 WATER TREATMENT CHEMICAL

The information contained herein is accurate to the best of our knowledge. However, data, safety standards and government regulations are subject to change; and the conditions of handling, use or misuse of the product are beyond our control. Carus Corporation makes no warranty, either express or implied, including any warranties of merchantability and fitness for a particular purpose. Carus also disclaims all liability for reliance on the completeness or confirming accuracy of any information included herein. Users should satisfy themselves that they are aware of all current data relevant to their particular uses.

##### CARUS  PHOSPHATES INC.

181 Woodlawn Ave  (  Belmont, NC 28012

Tel: (704) 822-1441   Fax: (704) 822-0922

E-Mail: salesmkt@caruscorporation.com

Web: www.caruscorporation.com

Copyright 2007

Form #PH

Rev. 107/07

CARUS™ 3350

Water Treatment Chemical

SHIPPING AND HANDLING

APPLICATION